## Slide 1: Troubleshooting
MercedEnergy.com
12-13-2018
Soldering
https://github.com/MercedEnergy/Soldering

## Slide 2: Cold Joint
Problem: Components not heated properly
Solution: Reheating Joints Closer

## Slide 3: Not Enough Solder
Bad Mechanical Connections
Solution : Reheat joint and add more solder.

## Slide 4: To Much Solder
Problem: Short out leads of other components
Solution : Remove using copper braid or solder sucker

## Slide 5: To Much Heat
May damage or melt PCB or components
Use less heat
  Cold joints are easier to fix

## Slide 6: To Much Movement
Disturbed joint
  Solder is not smooth
Solution: Use a third hand or PCB vise

## Slide 7: Wire Lead Soldered to PCB
Creates a short circuit
Solution: Do not bend leads more than 45 degrees
  Fix by removing solder

## Slide 8: Removing Solder
Reheat-and-Wipe
Copper Braid
Solder Sucker
  Small Vacuum Pump

## Slide 9: Thank You!
Ramiro Gonzalez
ramirogonzalez@mercedenergy.com

## Slide 10: Sources
Vinck, Marc De. Getting Started with Soldering: a Hands-on Guide to Making Electrical and Mechanical Connections. Maker Media, 2017.